## Slide 1
3D Printing:
Design, Print, Teach
Find or create a model, print it, then teach someone else how
Computer Science & Robotics | Grades 7-12

## Slide 2
The Project: 3 Steps
1
Find or Design
Download a model from Thingiverse or Printables, or design your own in Tinkercad
2
Print It
Use the MakerBot or Formlabs printer to bring your model to life
3
Teach It
Create a PowerPoint guide showing someone else how to use the printer

## Slide 3
MakerBot vs Formlabs
MakerBot (FDM)
Material: PLA filament (plastic spool)
Software: Ultimaker Digital Factory
Process: Export .makerbot file → USB → Print
Pros: Simple, fast, easy to remove prints
Cons: Visible layer lines, less detail
Formlabs (Resin/SLA)
Material: Liquid resin (hardens with UV light)
Software: PreForm
Process: Import STL → Send to printer → Wash → Cure
Pros: Smooth surface, high detail
Cons: Requires wash + cure, more steps

## Slide 4
MakerBot Printing Workflow
Get STL
Download from
Thingiverse/Printables
or export from Tinkercad
→
Slice It
Ultimaker Digital Factory
→ Import → Configure
→ Export .makerbot
→
Load Filament
Heat up → Feed spool
into tube → Push into
extruder until it oozes
→
Print
USB into printer
→ Select file
→ Watch first layers

## Slide 5
Key Vocabulary
Term | What It Means
STL File | Standard file format for 3D printing
Slicing | Converting a 3D model into printer instructions
PLA | Plastic filament used in MakerBot printers
Resin | Liquid material used in Formlabs (hardens with UV)
Build Plate | The surface the printer builds your object on
Supports | Temporary structures for overhanging parts
Post-Processing | Steps after printing: washing, curing, cleanup

## Slide 6
Your Mission
1
Find or design a 3D model (under 60 min print time)
2
Print it on MakerBot or Formlabs
3
Create a PowerPoint guide teaching someone else how
+5 bonus for designing your own model in Tinkercad!